## Slide 1: Optimization of intra-company transport and logistics processes within a selected enterprise
TRANSCOM 2025: 16th International Scientific Conference on Sustainable, Modern and Safe Transport
Dominik Benčo1,Iveta Kubasáková1, Peter Čauder1
1 Department of Road and Urban Transport, Faculty of Operation and Economics of Transport and Communications, University of Žilina, Univerzitná 8215/1, 010 26 Žilina, Slovakia
introduction |  | 
Intra-company transport involves the internal movement, loading, and unloading of materials using the company’s own handling equipment. Efficient vehicle utilization is essential for reducing costs and optimizing logistics operations. Enterprise XY, a leading Slovak appliance manufacturer, has expanded significantly, yet continues to rely on external haulers—making cost control and internal efficiency a key priority. | Despite increasing production and being a major player in the Slovak appliance market, Enterprise XY relies on external haulers and uses eight standard semi-trailers daily. This results in high operational costs, totaling €363,600 annually. The company lacks its own transport fleet, which limits its ability to optimize delivery operations effectively. | The objective of this study is to optimize intra-company transport by implementing an in-house fleet and transitioning from standard to MEGA semi-trailers. This change aims to reduce the number of trailers from eight to five and decrease annual costs by €56,752.20. The projected return on investment is approximately ten years. These results support long-term efficiency and sustainability.
materials, methods & implementation
The research employed a techno-economic modeling approach to optimize intra-company transport at Enterprise XY. The core objective was to determine the optimal number of vehicles required for material delivery within one work shift. Input data included daily material volumes, supplier distances, loading/unloading times, vehicle speed, and trailer capacity. Calculations were based on MEGA trailers (volume: 101 m³) with a load utilization coefficient of 0.9 and operating time of 8 hours per shift. A custom model was developed to calculate turnaround times and the number of required turnarounds per supplier, enabling precise vehicle allocation. The implementation phase involved creating a delivery schedule considering timing constraints, Labor Code regulations, and vehicle reusability across suppliers. Cost simulations were based on data from the Association of Road Haulers (ČESMAD Slovakia). The final setup proposed the use of five in-house MEGA semi-trailers instead of eight externally operated standard trailers, ensuring full delivery coverage within each 8-hour shift.
results
The optimization of intra-company transport at Enterprise XY led to a significant reduction in operational costs and vehicle usage. The transition from eight externally operated standard semi-trailers to five high-capacity MEGA trailers, owned and managed by the company, resulted in more efficient delivery scheduling and reduced fleet requirements. A daily transport volume of 2,516 m³ was handled using MEGA trailers with a capacity of 101 m³ and a utilization rate of 90%. Calculations based on turnaround times, loading/unloading durations, and distance to suppliers confirmed that five vehicles were sufficient to complete all deliveries within a standard 8-hour work shift. The economic evaluation showed that operating costs decreased from €1,600 per day (two shifts using external haulers) to €1,362.96 per day using in-house MEGA trailers. This yields annual cost savings of €56,752.20. The investment cost for five truck-trailer combinations was €587,500, resulting in an estimated return on investment of approximately 10.35 years. In addition, the new system allows for route consolidation, meaning some trailers can serve multiple suppliers. The optimization complies with Slovak labor legislation, as delivery distances are short and do not require regulated driving times or breaks. This change also increased planning flexibility and reduced dependency on external providers.
conclusion & implementation path
This study presented a comprehensive approach to optimizing intra-company transport at Enterprise XY by introducing an in-house fleet and replacing standard trailers with high-capacity MEGA semi-trailers. The proposed solution resulted in a reduction of trailers from eight to five, while fully covering transport needs within a single 8-hour shift. The optimization led to a calculated annual cost saving of €56,752.20 and an estimated investment payback period of approximately 10 years. The success of the proposal was achieved through detailed analysis of vehicle utilization, turnaround times, and cost modeling based on real operational data. The solution also accounted for scheduling constraints, social legislation, and logistical feasibility. The implementation of the new transport model not only improved internal efficiency but also strengthened the enterprise's strategic position by reducing dependence on external haulers and enhancing overall process control.
acknowledgements
This paper has been developed under support of the project MŠVVŠ SR VEGA No. 1/0686/25 KUBASÁKOVÁ I.: Application of Logistics 4.0 technologies in conjunction with other elements in the enterprise.
Operational Efficiency Daily volume: 2,516 m³ MEGA trailer capacity: 101 m³ Load utilization coefficient: 0.90 5 trailers now cover the entire workload Full deliveries completed within 8-hour shift Route consolidation between suppliers (e. g. A and D) |  | Investment & Benefits Investment: €587,500 (5 vehicles) ROI: approx. 10.35 years Short distances simplify logistics under labor law (No. 311/2001) Increased control, reliability, and independence Supports future sustainable upgrades (e. g. alternative fuel vehicles)
Chart: Cost Comparison
| Before Optimization | After Optimization
Daily Cost (€) | 1600 | 1362.96